## Slide 1
MINES | MEGN 301 — Mechanical Integration and Design
Technical Reference
Mechanical Power
Transmission
CHAINS, BELTS, GEARS, SHAFTS, LINKAGES, AND LINEAR/ROTARY MOTION SYSTEMS
Notes: Welcome to the Mechanical Power Transmission module for MEGN 301. Power transmission converts the torque and speed at a motor shaft into the force and velocity your mechanism needs. Every transmission element — belt, chain, gear, shaft, linkage, or lead screw — trades speed for torque and introduces losses. This module covers the complete toolkit for connecting motors to mechanisms.
ALIGNMENT NOTE — This module corresponds to Chapter 12 (Mechanical Power Transmission) of your Master Reference Document. Transmission specifications appear in your architecture block diagrams, trade studies, subsystem requirements, BOM, and ICDs.
FINAL NOTES — Key updates in the final compiled document: (1) This chapter now includes all gear reduction content previously in Ch 9 (Power Architecture). (2) NEW: Quick Decision Tree added to gear selection tip (hold position → worm/lead screw, precise linear → lead screw + stepper, fast linear → belt stage, etc.). (3) NEW: Sourcing guide with specific vendors (ServoCity, Pololu, SDP/SI, McMaster) and GT2 linear axis kit pricing ($15-25). (4) Practice question 7 includes a complete Caffeinated Creatures drive system design with motor sizing analysis.

## Slide 2
MINES | MEGN 301 — Mechanical Integration and Design
01
Fundamental
relationships
Power, torque, speed, gear ratio, and efficiency
Notes: Section 1 covers the fundamental equations that govern all mechanical power transmission.

## Slide 3
MINES | MEGN 301 — Mechanical Integration and Design
Power transmission fundamentals
Power is conserved (minus losses):
P = T × ω = F × v
T = torque (Nm), ω = angular velocity (rad/s), F = force (N), v = velocity (m/s)
Gear Ratio:
i = ωᵢₙ / ωₒᵤₜ = Tₒᵤₜ / (Tᵢₙ × η) = N_driven / N_driver
i > 1 = speed REDUCTION (torque multiplication) — most mechanisms need this
i < 1 = speed INCREASE (torque reduction)
Efficiency compounds multiplicatively:
Three stages at 95% each → 0.95³ = 85.7% overall. Minimize stages.
MINES | MEGN 301 — Mechanical Integration and Design
Notes: All mechanical power transmission obeys P = T times omega = F times v. The gear ratio i relates input and output speeds and torques. Most mechanisms need speed reduction because motors spin fast (1000 to 10000 RPM) but mechanisms need slow, forceful motion. The efficiency lesson is critical: losses compound multiplicatively. Three stages at 95% each give only 85.7% overall efficiency. Every unnecessary stage wastes energy as heat and adds complexity, cost, weight, and failure modes.

## Slide 4
MINES | MEGN 301 — Mechanical Integration and Design
02
Belt and chain
drives
V-belts, timing belts, roller chain: selection and sizing
Notes: Section 2 covers flexible-element drives — belts and chains that transmit power between shafts that may not be adjacent.

## Slide 5
MINES | MEGN 301 — Mechanical Integration and Design
Belt drive types
V-Belt — friction drive, wedge grip, 93-98% efficient
Slips under overload (acts as torque limiter). Absorbs shock. Requires re-tensioning.
Timing Belt (GT2/HTD) — toothed, positive engagement, 95-99% efficient
No slip. Precise positioning. No re-tensioning. DEFAULT FOR STUDENT PROJECTS.
GT2 Timing Belts for Student Projects
GT2 profile (2mm pitch) is the standard for hobby/prototyping
6mm or 10mm belt widths; 16T, 20T, 36T, 60T pulleys for 5mm motor shafts
20T driver + 60T driven = 3:1 reduction. Cost: $5-15 per axis.
Available: Amazon, Aliexpress, robotics suppliers (ServoCity, Pololu)
MINES | MEGN 301 — Mechanical Integration and Design
Notes: Two belt types dominate student projects. V-belts are friction drives that slip under overload — this can be a safety feature acting as a torque limiter. Timing belts have teeth that mesh with toothed pulleys, providing positive engagement with no slip. GT2 timing belts with 2mm pitch are the standard for hobby robotics and prototyping. They are inexpensive, widely available, and provide precise speed ratios. A 20-tooth driver pulley meshing with a 60-tooth driven pulley gives a 3:1 reduction — your motor speed is divided by 3 and your torque is multiplied by 3 times efficiency.

## Slide 6
MINES | MEGN 301 — Mechanical Integration and Design
Roller chain drives
Positive engagement like timing belts, but handles much higher loads
Standard sizes: #25 (1/4" pitch, ~100 lb), #35 (3/8", ~250 lb), #40 (1/2", ~500 lb)
Efficiency: 95-98%. Requires lubrication. Noisy at high speed.
Min 17 teeth on driver sprocket to avoid chordal action (speed pulsation)
Speed ratio up to 7:1 per stage
⚠ Chain requires lubrication and tensioning
Unlubricated chain wears rapidly — pins and bushings lose material, chain 'stretches', jumps teeth or breaks. Apply chain lube before every test session. Include adjustable tensioning in your mount design.
MINES | MEGN 301 — Mechanical Integration and Design
Notes: Roller chain provides positive engagement like timing belts but handles much higher loads. Chain is the go-to when belt capacity is insufficient or in dirty environments where belts degrade. The critical maintenance requirements: chain must be lubricated and tension must be adjustable. An unlubricated chain wears exponentially faster because the pins and bushings have no protective film. In student projects, apply chain oil before every test session and include a slot or adjustable mount for tension adjustment.

## Slide 7
MINES | MEGN 301 — Mechanical Integration and Design
03
Gear trains
Spur, helical, bevel, worm, and planetary gears
Notes: Section 3 covers gear trains — the most versatile and precise method for transmitting rotary power between shafts.

## Slide 8
MINES | MEGN 301 — Mechanical Integration and Design
Gear types comparison
Spur — parallel shafts, 94-98%, simplest, stock parts, noisy at high speed
Helical — parallel shafts, 94-98%, quieter than spur, creates axial thrust
Bevel — intersecting shafts (90°), 93-97%, right-angle drives
Worm — 90° non-intersecting, 40-90%, SELF-LOCKING, high ratio (5:1-100:1)
Planetary — coaxial, 90-97%, compact high-torque, pre-assembled gearboxes
For MEGN 301 Student Projects:
Option 1: Pre-assembled planetary gearbox ($25-80) — easiest integration
Option 2: Spur gears from ServoCity/Actobotics — most flexible
Option 3: 3D-printed gears — cheapest but lowest strength; use herringbone profile
MINES | MEGN 301 — Mechanical Integration and Design
Notes: Five gear types cover most applications. Two stand out for student projects: worm gears for applications requiring self-locking (the load cannot back-drive the motor), and planetary gearboxes for compact, high-ratio reduction. Pre-assembled planetary gearboxes that bolt directly to NEMA 17 stepper motors are available for 25 to 80 dollars and are the easiest path to gear reduction in a student project. For custom ratios, spur gears from robotics suppliers like ServoCity come with matching hubs and shafts. 3D-printed gears work for low-load applications but have limited strength — use herringbone profile to improve meshing and eliminate axial thrust.

## Slide 9
MINES | MEGN 301 — Mechanical Integration and Design
Worm gears: self-locking explained
Worm gear = helical screw (worm) meshing with a wheel
Very high ratios in single stage: 5:1 to 100:1
Self-Locking Property
When lead angle < friction angle (~6°), the load CANNOT back-drive the worm
Critical for: hoists, jacks, positioning stages — holds position without power
The Tradeoff: Efficiency
Same friction that enables self-locking means 40-70% efficiency
Lost energy becomes HEAT — may need cooling for continuous operation
Rule: if you need self-locking, accept the efficiency penalty
MINES | MEGN 301 — Mechanical Integration and Design
Notes: Worm gears are unique among gear types because of their self-locking property. When the worm's lead angle is below the friction angle — typically below about 6 degrees — the load physically cannot drive the worm backwards. This means the mechanism holds position without any motor current or brake. This is invaluable for applications like hoists where you want the load to stay in place when the motor stops. The tradeoff is efficiency: the same sliding friction that provides self-locking also wastes 30 to 60 percent of the input power as heat.

## Slide 10
MINES | MEGN 301 — Mechanical Integration and Design
04
Shafts, couplings
& linear motion
Shaft-hub connections, couplings, lead screws, and belt-driven stages
Notes: Section 4 covers the mechanical connections between rotating and linear elements.

## Slide 11
MINES | MEGN 301 — Mechanical Integration and Design
Shaft-hub connections and couplings
Shaft-Hub Torque Transmission
Set screws: simplest; slips under high torque; two at 90° better than one
Keyways: positive torque transfer; most reliable for moderate-to-high torque
Clamping hubs: split hub clamps shaft; no keyway needed; zero backlash
Press fits: interference fit; permanent; highest capacity
Shaft Couplings (connecting two shafts)
Rigid: zero misalignment tolerance; both shafts must be perfectly coaxial
Flexible jaw (Lovejoy): ~1° angular, 0.5mm parallel — good default for motors
Beam (helical): very flexible; zero backlash; precision CNC/3D printers
Universal joint: large angular misalignment (up to 45°); use in pairs
MINES | MEGN 301 — Mechanical Integration and Design
Notes: Shaft-hub connections transmit torque from a shaft to a gear, pulley, or other component. Set screws are the simplest but weakest — they rely on friction between the screw tip and the shaft. Keyways provide positive mechanical interlocking and are the standard for moderate to high torque applications. Clamping hubs from robotics suppliers like ServoCity are excellent for student projects because they provide zero-backlash clamping without needing to machine a keyway. For connecting two shafts, flexible jaw couplings are the best default choice — they accommodate the inevitable slight misalignment between a motor shaft and a gearbox or mechanism shaft.

## Slide 12
MINES | MEGN 301 — Mechanical Integration and Design
Linear motion systems
Lead Screw — rotary to linear, 30-50% efficient, SELF-LOCKING, high force, fine resolution
  2mm lead + 200 step/rev stepper = 0.01mm/step resolution
Ball Screw — 85-95% efficient, NOT self-locking, higher speed, more expensive
Rack & Pinion — fast linear, long travel, bidirectional, has backlash
Belt-Driven Stage — GT2 belt + linear rails, fast, quiet, lightweight
  Most common: 3D printer X/Y axes, desktop CNC, camera sliders
Slider-Crank — rotary to reciprocating, fixed stroke = 2× crank radius
Need position holding without power? → Lead screw or worm gear
Need speed? → Belt-driven stage or rack & pinion
MINES | MEGN 301 — Mechanical Integration and Design
Notes: Five methods convert rotary to linear motion. Lead screws provide the highest force and finest resolution with self-locking — ideal for Z-axes and positioning where you need to hold position without power. Ball screws are much more efficient but not self-locking — the load will back-drive the motor. Belt-driven stages are the fastest and lightest but cannot hold position. For student projects: if you need precise positioning with holding (like a vertical lift), use a lead screw. If you need fast horizontal motion (like a gantry), use a GT2 belt stage on linear rails.

## Slide 13
MINES | MEGN 301 — Mechanical Integration and Design
Linkages: four-bar and slider-crank
Four-Bar Linkage — most fundamental planar mechanism
4 rigid links + 4 pin joints. Varying link lengths produces:
  Crank-rocker: one link rotates, other oscillates
  Double-crank: both rotate fully
  Double-rocker: both oscillate
Grashof criterion: s + l ≤ p + q for at least one full-rotating link
Slider-Crank — rotary ↔ reciprocating linear
Crank + connecting rod + slider. Stroke = 2 × crank radius.
Every piston engine, reciprocating compressor, and many packaging machines.
MINES | MEGN 301 — Mechanical Integration and Design
Notes: Linkages are mechanisms made of rigid links connected by joints. The four-bar linkage is the fundamental building block — by changing the relative lengths of the four links, you can produce rocking, rotating, or oscillating motion. Grashof's criterion predicts the mechanism type from link lengths. The slider-crank converts rotation to reciprocating linear motion and is the mechanism inside every piston engine. While linkages are less common in student projects than belt or gear drives, understanding them is essential for mechanism design.

## Slide 14
MINES | MEGN 301 — Mechanical Integration and Design
Selection framework and design rules
Speed reduction, parallel shafts → Timing belt or planetary gearbox
Speed reduction, right angle → Bevel or worm gear
High ratio, compact → Planetary gearbox or worm gear
Precise linear positioning → Lead screw + stepper
Fast linear motion → Belt-driven stage or rack & pinion
Hold position without power → Worm gear or lead screw (self-locking)
Absorb shock/misalignment → V-belt or flexible coupling
ALWAYS: Calculate required output torque/force FIRST, then size the transmission backwards to the motor.
MINES | MEGN 301 — Mechanical Integration and Design
Notes: The selection framework starts from your output requirement and works backwards to the motor. First, define the load: what torque, speed, force, or velocity does your mechanism need? Second, calculate the required gear ratio and power. Third, select the transmission type based on shaft arrangement, efficiency needs, and whether self-locking is required. Fourth, size components using catalog ratings. Fifth, verify that the motor can supply the required power including all transmission losses. The most common student error is selecting a motor first and then discovering it cannot deliver enough torque through the transmission to the load.